ARCOPOL Waste Management Guide Overview

Guidance on Waste Management during a shoreline pollution incident. Operational Guidelines – Guideline Overview

Project: ARCOPOL
Date of Release: 12/2011
Type:	Guide
Author: Cedre
Responsible Partner: Cedre
Partners: Pembrokeshire County Council and Environment Agency Wales.

Brief Description:
In the event of an accidental shoreline pollution incident, clean-up operations inevitably generate a variety of waste materials, sometimes in great quantities. The management of waste, up to and including its final disposal, and the complete restoration of all sites can cause major problems for responders. The options chosen must be in accordance with the regulations in force and ensure traceability throughout the entire chain. Communication should be rapid, accurate and transparent.
The aim of this guide is to assist decision makers and operational responders in the initial stages of the emergency response by providing them with concise information on all aspects and phases of waste management following a maritime pollution incident.
This guidance focuses in certain areas on oily waste, but the principles should also be applied to the management of hazardous and noxious substances (HNS) and large quantities of nonpolluting waste (e.g. timber/plastics) resulting from maritime incidents.
This guide is intended for responders and managers working within strategic and tactical response groups as well as operational responders on the ground.

Table of Contents:
Purpose of this guide	4
Structure	6
Regulatory Context	7
Waste Management Strategy	15
Practical datasheets	31
Feedback datasheets	55
Futher Information	77